## Slide 1
Analysis of Mice/Elephant Flow Prioritization Using DB Workloads

## Slide 2
Introduction
Cisco Nexus 9000 switches can be configured to prioritize mice flows over elephant flows. The objective of the tests was to simulate workloads that are typically used in enterprises and analyze performance improvement for these workloads due to the impact of prioritization
Criteria used by Nexus 9000 to prioritize
  Definition of a flow: Tuple (Src_IP, Src_Port,Dest_IP, Dest_Port)
  If 2 consecutive transactions of the same tuple are less than 5 ms apart, the two transactions would be considered part of the same flow. A flow would break only if the inter-packet interval exceeds 5 ms
  The first 10 packets of a flow are sent to a high priority no-drop queue and the subsequent packets would be sent to the drop queue
In order for impact of prioritization by Nexus 9000 to be apparent, following criteria has to be met:
  Traffic from multiple ports must sink into a destination port
  The destination port should be saturated
  Server attached to the destination port should not drop packets and regulate the flow. Rather, the server should have sufficient TCP buffer size to avoid server side loss and lead to queue build up on the switch size thereby causing the switch to initiate flow control

## Slide 3
Workload Description
Nexus 9000
Postgres
(Small)
Postgres
(Large)
HammerDB
Load Gen
ElasticSearch
Based PerfMon
2 instances of Postgres databases are setup. Field sizes for these DBs are tuned such that each DB produces different payload size when queried
  Small: 8KB
  Large: 32MB
HammerDB is used to generate load on the two databases. Two instances of HammerDB are run in the HammerDB server
Total number of transactions on HammerDB node are adjusted such that each flow independently finishes in 2 min. If the two flows were run simultaneously, they would complete in approx 4 mins.
The two loads are sufficient to saturate the 10G link on HammerDB node
The network traffic is captured through scripts and stored on ElasticSearch server for analysis. Parameters captured include:
  Switch Port Tx Rate, Tx Pause, Tx Drops
  Switch Port Rx Rate, Rx Pause, Rx Drops
  Switch Port Buffer Utilization
  Server side Rx Drop, Tx Drop
  Server Side TCP Retrans, TCP Reset

## Slide 4
Switch Configurations
Tests were conducted for Evergreen release
Dpp configuration steps:
====================
n9k-125# conf t
Enter configuration commands, one per line. End with CNTL/Z.
n9k-125(config)# policy-map type network-qos dpp-nwqos
n9k-125(config-pmap-nqos)# class type network-qos c-8q
c-8q-nq-default c-8q-nq1 c-8q-nq2 c-8q-nq3 c-8q-nq4 c-8q-nq5 c-8q-nq6 c-8q-nq7
n9k-125(config-pmap-nqos)# class type network-qos c-8q-nq?
c-8q-nq-default Default class on qos-group 0
c-8q-nq1 Default class on qos-group 1
c-8q-nq2 Default class on qos-group 2
c-8q-nq3 Default class on qos-group 3
c-8q-nq4 Default class on qos-group 4
c-8q-nq5 Default class on qos-group 5
c-8q-nq6 Default class on qos-group 6
c-8q-nq7 Default class on qos-group 7
n9k-125(config-pmap-nqos)# class type network-qos c-8q-nq-default
n9k-125(config-pmap-nqos-c)# dpp ?
set-qos-group QoS group to be mapped
n9k-125(config-pmap-nqos-c)# dpp set-qos-group ?
<0-7> QoS Group Value
n9k-125(config-pmap-nqos-c)# dpp set-qos-group 7 ?
<CR>
n9k-125(config-pmap-nqos-c)# dpp set-qos-group 7
n9k-125(config-pmap-nqos-c)# end
n9k-125# conf t
Enter configuration commands, one per line. End with CNTL/Z.
n9k-125(config)# system qos
n9k-125(config-sys-qos)# service-policy type network-qos dpp-nwqos
n9k-125(config-sys-qos)# end
n9k-125#

## Slide 5
Results
 | Small flow completion time | Large flow completion time
Without Dpp configuration | 4.5 | 2.5
With Dpp configuration | 2.6 | 4.4